## Slide 1
Murray Gray Alberta Innovates Thursday May 26, 2022
NPUC Workshop: Advances in Bitumen Processing

## Slide 2: Workshop Objectives
  Inform NPUC members and the Alberta research community on new directions in basic science and emerging technologies for more selective upgrading of bitumen, including:
  a. Selective pathways for sulfur and metals removal
  b. Processing without addition of hydrogen
  2. Inform researchers of industry needs and new directions in bitumen processing

## Slide 3: Workshop Steering Committee

## Slide 4: Workshop Agenda
  Opening Remarks (Murray Gray)
  Industry Perspectives – Panel Discussion
  (Moderator: Shunlan Liu, Alberta Innovates)
  Session 1: Processes based on new reaction pathways (Chair: Mohamed Ali, CANMET Energy)
  Lunch Break
  Session 2: New fundamentals for bitumen processing (Danuta Sztukowski, CNRL)
  Poster Session – Eight simultaneous Teams sessions
  Workshop Close – at 15:10 please rejoin the main link

## Slide 5
National Partial Upgrading Committee (NPUC)
Established in 2015 as a collaborative program
Oilsands producers and government agencies
Partial Upgrading  reducing diluent for bitumen pipeline transport
Collaborations include:
Sharing of technical and scientific information
Policy and market studies
Regulations and specificiations on oilsands products

## Slide 6: Current Oilsands Operations
Deep Conversion Refinery
Pipeline
Upgrader
Production
Pipeline
Refinery
Full Upgrading to Synthetic Crude Oil (SCO)
Diluted Bitumen Shipment to Refineries
CNRL
Suncor, Cenovus
CNRL, MEG
Cenovus, Imperial Oil, Suncor
SCO
Dilbit
Production
Diluent to reduce viscosity
(Significant volume recycled via pipeline and reused)

## Slide 7: Expanding Scope of Bitumen Processing
Partial
Upgrader
Bitumen or
Bitumen Emulsion
Partially Upgraded Bitumen
Diluent
Asphaltenes
Carbon fibres
Carbon materials
Binders and adhesives
Coatings
Sequestration
Vanadium
Bitumen Beyond Combustion
Partial Upgrading
Imperial Oil Kearl
Suncor/Teck Fort Hills
New technologies nearing commercialization

## Slide 8: Refinery Processes – High Conversion Refinery

## Slide 9: Bitumen Upgrading Overlaps with Refining
Units used in Alberta upgraders or proposed for partial upgraders

## Slide 10: Capital costs for refining and upgrading
Full upgraders cost over $60K/BBL/d
Target for partial upgrading under $30K/BBL/d
Northwest Refinery cost $ 124K/BBL dilbit/d
Supporting facilities can be ½ total cost or more
Northwest Sturgeon Refinery
Processing equipment

## Slide 11: GHG Emissions from Upgrading
Pacheco et al., 2019
Hydroconversion
Shell/CNRL
Delayed coking
Suncor, CNRL Horizon
Fluid coking + Hydroconversion, Syncrude

## Slide 12: Range of Bitumen Components
Vacuum residue
VGO
Atmospheric
distillate
Bitumen contains over 50% vacuum residue
Molecular weight to over 1200
C40 to C60
Up to 4 sulfur atoms per molecule
N, Ni, V
C14

## Slide 13: Current Commercial Options for Processing of Vacuum Residue (VR)
Vacuum Residue
Separate by Distillation or Solvent Separation
Fuel Oils
Asphalt Binders
Thermal Cracking, T>390°C
Visbreaking
(Mild Thermal Cracking)
Coking
Hydroconversion
FCC
Two-step processes – thermal cracking then catalysis of fragments
Asphaltene precipitated for
sequestration or fuel

## Slide 14: Why is heat is the main option for largest molecules?
80-90 wt% bridged structures
Strong aggregation
10-20 wt% large aromatic groups
Weak aggregation
Non-Contact AFM images from Schuler et al., Energy and Fuels, 2017
Concentrations from Chacon-Patino et al., Energy and Fuels, 2018

## Slide 15: Thermal Cracking
Vacuum Residue
Bond Breakage
Molecular Rearrangement
Addition
Methane, ethane, propane
Coke
Olefins (ethylene etc.)
Distillates (C5 to C40)
Unconverted VR (C40 to C60)
Extremely complex reactions
Very limited control over products
  Time and temperature  “severity”
  Recycle
Heat to > 390°C

## Slide 16: Hydroconversion – Catalyst Plus Hydrogen
Vacuum Residue
Bond Breakage
Molecular Rearrangement
Addition
Methane, ethane, propane
Coke
Olefins (ethylene etc.)
Distillates (C5 to C40)
Unconverted VR (C40 to C60)
Same thermal reactions
Catalyst + hydrogen gives benefits
  Suppress coke formation
  Convert olefins and some sulfur
Consumables and equipment are very expensive
Heat to > 420°C


Catalytic sulfur removal

## Slide 17: Specifications for Refining Versus BBC
Application | Important Properties
Pipeline transport | Viscosity at 10-30°C, density, solids, water, olefins
Refining to liquid transport fuels | Stability of asphaltenes, fouling tendency, yields in refinery processes
Carbon Fibre Feeds | Rheology at 150-300°C, Organic solids content, Ability to graphitize, Sulfur, Metals
Asphalt binder feeds | Rheology at -40 to +50°C, Compatibility with polymers, Adhesion, Wax separation, …
High Value Carbon Materials | Unique to each product

## Slide 18: Workshop Agenda
  Industry Perspectives – Panel Discussion
  (Moderator: Shunlan Liu, Alberta Innovates)
  Session 1: Processes based on new reaction pathways (Chair: Mohamed Ali, CANMET Energy)
  Lunch Break
  Session 2: New fundamentals for bitumen processing (Chair: Danuta Sztukowski, CNRL)
  Poster Session – Eight simultaneous Teams sessions
  Workshop Close – at 15:10 please rejoin the main link
  Q&A Sessions: Please use the “Chat” function to indicate that you have a question, and for whom